## Slide 1
IITK
BATMAN-ADV MESH NETWORKING, DRONECAN-BASED ESC FIRMWARE & SAD-BASED OPTICAL FLOW STABILIZATION ON LOW-COST EMBEDDED HARDWARE
Arya Sanchihar (Roll No. S260036) • Dept. of Electronics & Communication Engineering, IIT Kanpur
SURGE Intern, Department of Electrical Engineering, IIT Kanpur • Mentor: Prof. Ketan Rajawat
COMMS
ACTUATION
VISION
MOTIVATION
Battlefield communication cannot depend on centralized infrastructure that adversaries can target physically or through electronic warfare. A soldier-wearable platform instead needs infrastructure-independent networking, robust low-level actuation, and stabilized real-time vision — three complementary subsystems, developed and validated independently, presented together here.
COMMS
BATMAN-ADV MESH VIDEO NETWORK
Infrastructure-independent P2P streaming across Raspberry Pi nodes
PROBLEM STATEMENT
Centralized comms (cellular, fixed Wi-Fi APs) create a single point of failure in a contested environment. A soldier-worn camera and multi-Pi mesh must route peer-to-peer video and telemetry with no central control, gracefully handling nodes joining, leaving, or moving out of range.
METHODOLOGY
Layer-2 mesh: B.A.T.M.A.N.-Adv over ad-hoc wlan0, joined into a bat0 virtual-switch interface
Zero-config forwarding: Avahi mDNS link-local IPs — no DHCP server required
Video path: GStreamer producer/consumer, H.264 over RTP/UDP; GTK receiver; suppressed monitoring UI
Validated first in a 3-container Docker simulation, then on 3 physical Raspberry Pi nodes (Pi 4 + Pi 5) with on-node OSD displays
RESULTS
Mesh routing diagram
(Pi1–Pi6 nodes)
Logical routing paths through mesh nodes & interfaces, illustrating best-next-hop selection independent of centralized routing.
NOVELTY
Operates at the data-link layer, not IP — the whole mesh presents as one virtual switch, so every node need only find its best next hop rather than compute a full path. Combined with DHCP-free Avahi addressing, this gives fully self-organizing, infrastructure-independent bring-up, with each node doubling as both a relay and a local display endpoint.
GTK MONITORING UI
A custom GTK4 desktop client drives the GStreamer consumer pipeline (rtph264depay → avdec_h264 → gtksink) for live per-node video preview. Each Pi runs the matching producer pipeline (v4l2src → x264enc → rtph264pay → udpsink) that feeds the mesh.
Insert UI screenshot here
ACTUATION
DRONECAN-STAGED ESC FIRMWARE
Sensorless BLDC control on STM32F303RET6 + DRV8353S
PROBLEM STATEMENT
A compact actuator needs sensorless motor control with no Hall or encoder wiring, a standardized command bus (DroneCAN) for future flight-controller compatibility, onboard safety telemetry, and field-updatable firmware — all while Cortex-capable test hardware was not yet available during bring-up.
METHODOLOGY
Platform: STM32F303RET6 (72 MHz) + DRV8353S 3-phase gate driver over SPI
Control: sensorless six-step trapezoidal commutation, zero-crossing detection, >34 kHz PWM (ARR = 2099)
Staged command bus: PWM input → validated DroneCAN RawCommand via libcanard → pending hardware
Ramped apply_throttle() (RAMP_STEP = 3 counts/ms) with watchdog-driven safe-state cutoff on command timeout
Read Command (PWM / validated / CAN pending)
↓
Watchdog Interval Check
↓
6-Step Commutation via BEMF Zero-Cross
↓
Fault? → Safe State | OK → Report Telemetry
RESULTS
Throttle @ throttle = 40% (full-scale, 12-bit)
PWM out @ pwm_pulse_us = 1500 µs, confirmed via TIMx CCR1 → 1500-count pulse width
Switching @ >34 kHz, 6-channel complementary gate drive
Safety @ Overcurrent/Undervoltage/ADC checks → SPI driver fault reporting (fault injection testing pending)
Input-capture end-to-end mapping confirmed correct on real hardware; full six-step commutation and safety control loop are functionally complete on the Nucleo-64 board.
NOVELTY
A staged bring-up architecture lets the safety and commutation logic get proven end-to-end on real hardware entirely decoupled from CAN bus availability — the same firmware core swaps its command source (PWM → DroneCAN) without touching the validated commutation or watchdog logic.
VISION
SAD OPTICAL FLOW + EIS
Real-time adjacent stabilization on a 64 KB RAM Cortex-M4
PROBLEM STATEMENT
Dense optical flow (Lucas-Kanade, Horn-Schunck) needs iterative solving and heavy CPU/RAM — infeasible on a Cortex-M4 with 64 KB RAM and no hardware float throughput. A stabilized real-time feed still needs reliable per-frame motion estimation on this hardware.
METHODOLOGY
SAD block-matching, integer-only, accelerated with Cortex-M4 SIMD (4 abs-diffs/cycle)
Pipeline: variance-based low-texture rejection → full-search SAD → histogram outlier filter → subpixel parabolic refinement → 2D Kalman smoothing → EIS crop-correction
Benchmarked on STM32F303RE (Nucleo-64) against the MPI-Sintel dataset (Middlebury "Army" had insufficient motion for reliable detection)
Compiler opt: -O2, reduced search radius (ρ = 6) and variance threshold (50 → 15) tuned for the 64 KB RAM budget
RESULTS — 11 FRAME PAIRS (MPI-SINTEL)
19.6 FPS
Mean frame rate (95% C.I.)
51.2 ms
Mean frame time (95% C.I.)
100%
Valid blocks (ρ/θ), mean
66.5 / 100
Pixel coincidence score (mean)
Chart: Horizontal Motion (v_x)
| P1 | P2 | P3 | P4 | P5
SAD (on-device) | -2.1 | -3.4 | -1.2 | -4 | -2.8
Farneback (reference) | -1.9 | -3.1 | -1.4 | -3.7 | -2.5
Fig. On-device SAD motion estimate vs. Farneback dense optical-flow reference, per frame pair.
NOVELTY
Runs a complete 6-stage optical-flow + EIS pipeline — not just raw block matching — at a sustained ~19.6 FPS entirely on a sub-$10-class MCU, with SIMD-accelerated integer SAD replacing a dense float solver and search-radius/variance tuning trading a small, quantified accuracy margin for throughput headroom under a hard 64 KB RAM ceiling.
SYSTEM INTEGRATION & CONCLUSION
Though developed and tested largely independently, the three subsystems form complementary layers of one soldier-wearable platform: mesh comms for infrastructure-free video/telemetry, ESC firmware for low-level actuation, and SAD-based EIS for stabilized vision. The consistent lesson across all three: decouple a subsystem's core logic from hardware or infrastructure that may be temporarily unavailable — Docker-simulated mesh nodes standing in for physical hardware, and a validated PWM path standing in for DroneCAN while CAN-capable test hardware was unavailable — so development stays productive without hardware in hand.
FUTURE WORK
End-to-end DroneCAN RawCommand validation for motor drive
Multi-node mesh field testing under realistic RF interference
Migrate ESC control from six-step to field-oriented control (FOC)
5–10 km soldier-node hops via directional / sub-GHz radios with multi-hop batman-adv relay
REFERENCES
[1] A. Neumann, C. Aichele, M. Lindner, S. Wunderlich, "Better Approach to Mobile Ad-hoc Networking (B.A.T.M.A.N.)," IETF Internet Draft, Mar. 2008.
[2] L. Lin, J. Liu, H. Qian, J. Zhu, "Performance Evaluation of BATMAN-Adv Wireless Mesh Network Routing Algorithms," CSCloud/EdgeCom, 2018, pp. 122–127.
[3] "Multi-link-optimize," B.A.T.M.A.N. Advanced Wiki, Open Mesh.
[4] PX4/Zubax, "Sapog ESC Firmware," PX4 Guide — DroneCAN Documentation.
[5] AlibAliMoses, "AM32-MultiRotor-ESC-firmware," GitHub repository.
[6] A. Garcia-Dopico, J. L. Pedraza, M. Nieto, A. Perez, S. Rodriguez, J. Nava, "Parallelization of the optical flow computation in sequences from moving cameras," EURASIP J. Image and Video Processing, vol. 2014, art. 18, 2014.
[7] J. Butles, J. Wulff, G. B. Stanley, M. J. Black, "A naturalistic open source movie for optical flow evaluation," ECCV, 2012, pp. 611–625.